## Slide 1: Air Traffic Control System
Chapter 3 Section B

## Slide 2: Air Route Traffic Control Center
Provides nationwide traffic separation during all phases of IFR flight using a network of radar and non-radar facilities.
  Including air traffic control centers, approach control, and departure control, control towers, ground controls, and clearance deliveries.

## Slide 3: ARTCC Traffic Separation
Separates IFR traffic from VFR aircraft and provides advisories to VFR aircraft on a work-load permitting basis.

## Slide 4: Processing the IFR Flight Plan
Weather conditions are below VFR minimums
Must submit flight plan to an AFSS or an air traffic control tower; by telephone or radio.
Can also file domestic VFR and IFR flight plans through DUATS.
Due to the time it takes to check all variables, flight plans should be filed at least 30 minutes prior to intended departure time.
After Flight Plan is processed, the clearance will be ready when you call ATC at your departure airport.

## Slide 5: Weather Information
Reports include
  AIRMETs, SIGMETs, Convective SIGMETs, urgent pilot weather reports (UUA) and Center Weather Advisories (CWAs)
Two types of radar systems available to controllers to assist pilots in avoiding convective weather inflight
  Airport Surveillance Radar (ASR)
    Used by approach controllers to advise pilots of four levels of precipitation intensity
      Light, moderate, heavy, and extreme
  Weather and Radar Processor(WARP)
    Used by Center Controllers to notify pilots of three levels of precipitation intensity:
      Moderate, heavy, and extreme

## Slide 6: Safety Alerts
Issued by Center Controller when it becomes apparent that your flight is in unsafe proximity to terrain , obstructions, or other aircraft.
Terrain or Obstruction Alert: is issued when Mode C altitude readout indicates your flight is below published minimum safe altitude for that area.
Figure 3-30

## Slide 7: Emergency Assistance
If problem arises ATC is immediately available to render a wide variety of services:
  Clearing conflicting traffic or giving priority to aircraft in emergency situations.
  Providing radar vectors and, if required, a radar approach to the nearest suitable airport
  Alerting search and rescue (SAR) agencies in the area.

## Slide 8: Terminal Facilities
Within air traffic control system, each terminal facility is closely linked with the associated ARTCC to integrate the flow of IFR departures and arrivals.
Include:
  ATIS, Ground Control, Clearance Delivery, Control Tower, Approach, and Departure Control, and FSS.

## Slide 9: ATIS
Automatic Terminal Information Service
Continuous, recorded broadcast of non-control information helps to improve control tower effectiveness and to reduce frequency congestion.
Updated whenever any official weather is received, regardless of content change.

## Slide 10: Clearance Delivery
In order to relieve congestion on ground control frequency at busier airports, a discrete clearance delivery may be provided.

## Slide 11: Control Tower
Responsible for the safe, orderly, and expeditious flow of all traffic which is landing, taking off, operating on and in the vicinity of an airport.
Movement Areas: defined as runways, taxiways, and other areas which are used for taxiing, takeoffs, and landings, exclusive for loading ramps and parking areas.

## Slide 12: Approach and Departure Control
Coordinate very closely with the ARTCC to integrate arrival traffic from the enroute stage to the terminal area, and transition departure traffic to the enroute phase.
These services are designated as either basic or TRSS (terminal radar service area) service.

## Slide 13: Radar Service for VFR Aircraft
Basic Radar Service: provides safety alerts, traffic advisories, limited vectoring, and sequencing at certain locations.
TRSA Service: includes radar vectoring, sequencing, and separation for all IFR and participating VFR aircraft.

## Slide 14: Flight Service Stations
Conduct weather briefings and handling flight plans, provide local airport advisory (LAA)s

## Slide 15: Works Cited
Jeppesen. Guided Flight Discovery: Instrument Commercial. Englewood, CO, 2013.